## Slide 1: Home Camera-Based Fall Detection System for the Elderly
Koldo de Miguel, Alberto Brunete, Miguel Hernando and Ernesto Gambao
Multidisciplinary Digital Publishing Institute (MDPI)
Sensors 2017

## Slide 2: abstract
fall detectors based on artificial vision
low cost
-> not yet available on the market
Using
background subtraction
Kalman filtering and optical flow

## Slide 3: 1. introduce
7 million dementia patients in Europe alone
double every 20 years
improves their independence, comfort and safety and prevents depression
frees caregivers

## Slide 4
Accident detect -> send message
low-cost device like a Raspberry Pi

## Slide 5: 2.1 wearable sensors
Use accelerometers and gyroscopes
inside the wearer’s ear.
electromyographic (EMG) sensors (근전도)

## Slide 6: 2.2. Ambient Devices
vibration sensors
laser-emitting component
Audio
Wearable airbag

## Slide 7: 2.3. Vision-Based Devices
sends only images when the fall has been detected.
merge cameras (Microsoft’s Kinect) and accelerometera

## Slide 8: 2.3.1. Cameras
body and shape change, posture detection, inactivity, spatiotemporal and 3D head change.

## Slide 9: 2.3.2. Processing Units
high computational processing power
expensive hardware
This paper use Raspberry Pi

## Slide 10: 2.3.3. Relevant Information Segmentation
subtraction of a background image
identify certain features of the human body(ex. Head)

## Slide 11: 2.3.4. Subject Tracking
simplified colour based algorithm
person’s head, body and legs are easily differentiable

## Slide 12: 2.3.5. Data Modelling
rectangles and ellipses -> easy sampling

## Slide 13: 2.3.6. State Classification
rules and data thresholds
K-Nearest Neighbours and Support Vector Machines
Artificial Neural Networks and Hidden Markov Models

## Slide 14: 3. Description of the Hardware

## Slide 15: 4. Fall Detection Algorithm

## Slide 16: 4.1. Data Model
The angle refers to the angle between the x-axis and the major-axis of an ellipse enclosing the subject.
The ratio refers to the relationship between the width and height of a rectangle that encloses the subject.

## Slide 18: 4.2. Background Subtractor

## Slide 19: 4.3. Kalman Filter

## Slide 21: 4.4. Optical Flow
sensitive enough to detect even small movements

## Slide 22: 4.5. State Classification
The KNN algorithm
the angle
subject ratio
three most recent values for ratio change speed as input.

## Slide 23: Twofold(ratio speed change)
weighted to reduce the influence of the otherwise triplicated ratio change speed
the addition of a calmness condition to the fallen state
(small movements to seizure-like movements)
avoids inconsistent state transition phases

## Slide 24
Future version use support vector machines (SVM)

## Slide 25: 4.6. Occlusions

## Slide 26: 4.7. Alert System

## Slide 27: 5. System Installation
Camera installed at height of 2 to 2.25 m , 14◦± 5◦
Must not towards TVs or reflective objects and bright windows
The entire flat can be covered with six cameras.

## Slide 29: 6. Results and Discussion

## Slide 32
different algorithms
->> other states such as walking and sitting.