## Slide 1: A New Method for Fall Detection of Elderly Based on Human Shape and Motion Variation
Abderrazak Iazzi, Mohammed Rziza, Rachid Oulad Haj Thami, and Driss Aboutajdine
International Symposium on Visual Computing ISVC 2016

## Slide 2: abstract
the person shape -> three blocks extracted from rectangle
using thresholding-based method

## Slide 3: introduction
computer-vision-based fall detection system
use scene analysis to identify a laying posture
vector analysis to identify abnormal motion

## Slide 4: Related Work
extracted from the three points (centroid of upper, middle and lower human part)
fall detection through SVM and AdaBoost classiﬁcation

## Slide 5
Online one class Support Vector Machine (OCSVM) Model
-distinguish a normal posture from an abnormal posture

## Slide 6: The Principal Module of Fall Detection System
(i) video capture
(ii) Detection Moving Object
(iii) Features Extraction and
(iv) Recognition Behavior and fall detection.

## Slide 8: Background Subtraction
use the CB(codebook) method
capability of removing shadows
->>Distinguish person from background
BS results obtained contain diﬀerent noisy artifacts

## Slide 9: Post-Processing
result obtained is not always satisfying in general
BLOB-merging : a number of pixels of their area less than a threshold should be removed. Ex) 50px
Determining the Human Silhouette : two objects have nearly the same number of moving pixels
Notes: the smallest distance between its position (center of gravity) and the last recorded position of the person.

## Slide 11: compute the person’s velocity
three blocks based on the width and height

## Slide 12: Fall Detection
The abnormal event is characterized by a sudden change in velocity and shape
the normal activities take more time

## Slide 13: Experimental Results
Dataset is composed of 219 videos, including diﬀerent activities, 95 videos of normal activities and 124 videos of fall activities

## Slide 14: Background Subtraction Results

## Slide 15: Feature Analysis and Fall Detection
Between 3 boxes
Width / height

## Slide 17: Performance of Our Fall Detection System
TP FALL > DETECT
FP FALL > NOT DETECT
TN NOT FALL > NOT DETECT
FN NOT FALL > DETECT

## Slide 19
need to improve the background subtraction
-> only rely on the motion and the distance between objects
only made under good lighting conditions
depends on the best thresholds used to detect a fall
Conclusion and Discussion